## Slide 1
MODEL PREDICTIVE CONTROL · GNC
Guided Parafoil Recovery
An MPC-based guidance and control stack that steers a deployed parafoil back to the launch pad under real wind — and a simpler fallback that flies when the optimiser cannot.
Project Luna · Rocketry GNC · Technical Review
6-DOF
simulator + LTV-QP MPC
2 tracks
primary MPC · fallback guidance
OSQP
embedded solver target

## Slide 2
MISSION
Bring the vehicle home, predictably
Develop an autonomous guided parafoil recovery system for a rocketry team: steer the deployed parafoil back to the launch pad under real-world wind disturbances.
The project spans GNC algorithm development, mechanical and actuator design, and eventual deployment on flight hardware.
Theoretical rigor
A simulation-validated MPC-based guidance and control stack.
Practical trustworthiness
A system that behaves predictably on real flight hardware — and fails gracefully when it does not.
These are treated as distinct engineering goals requiring different design choices — not two labels for the same work.
Luna · Guided Parafoil Recovery
2 / 16

## Slide 3
STRATEGY
Two parallel tracks, deliberately
A higher-fidelity primary approach and a simpler, more robust fallback are maintained at the same time. Neither blocks the other.
Track A — Primary: MPC
Nonlinear receding-horizon optimisation over the parafoil model.
Highest performance and the research vehicle for the project.
Carries solver, compute, and tuning risk onto flight hardware.
Validated first in a 6-DOF Python simulator.
Track B — Fallback: phased waypoint guidance
Deterministic guidance law, no optimiser in the loop.
The reliable option for flight hardware.
Predictable failure behaviour and trivially auditable.
Developed in parallel, not as a post-hoc backup.
Rule of thumb: the track that flies is the one you can explain to the range safety officer.
Luna · Guided Parafoil Recovery
3 / 16

## Slide 4
SCOPE
Technical domains in play
Model predictive control and trajectory optimisation
Receding-horizon formulation, constraints, solver selection.
Guidance law design
Phased waypoint guidance as the robust flight-hardware path.
Wind estimation
Recovering the disturbance the controller is fighting.
Parafoil flight modelling
Kinematic and dynamic models, up to 6-DOF with apparent mass.
Actuator and mechanical design
Servo and brake/control-line system, shock-load protection.
Luna · Guided Parafoil Recovery
4 / 16

## Slide 5
ARCHITECTURE
The closed loop, end to end
Sensing
GPS, baro, IMU
Estimation
State + wind estimate
Guidance
Target / reference path
Control
MPC or waypoint law
Actuation
Brake-line servo
Feedback closes the loop every timestep — the plan is recomputed, not replayed.
Plant model
Parafoil dynamics integrated with a fixed-step RK4 scheme, driven by a wind model.
Validation
Closed-loop simulation across calm, steady-wind, shear/turbulence, and gust scenarios.
Luna · Guided Parafoil Recovery
5 / 16

## Slide 6
KEY INSIGHT
MPC's practical robustness comes from receding-horizon feedback on measured state — not from model accuracy.
This reframes where effort belongs. Chasing model fidelity has diminishing returns; guaranteeing that the loop re-solves on fresh state, on time, every timestep, does not. It also explains why a coarse model plus fast feedback beats a beautiful model solved too slowly to matter.
Luna · Guided Parafoil Recovery
6 / 16

## Slide 7
CURRENT IMPLEMENTATION
MPC formulation as it stands
Nonlinear receding-horizon optimal control
Re-solved each timestep from the current measured state.
MATLAB `fmincon` with SQP as the solver
Accurate, flexible with nonlinear constraints, and compute-hungry.
Custom fixed-step RK4 prediction model
Deterministic step cost, which matters for embedded budgeting.
Wind disturbance model in the loop
The controller is evaluated against the disturbance it must reject.
Why this is a development-only choice
`fmincon`/SQP iterates linearise → solve → step until convergence.
Iteration count is data-dependent, so worst-case runtime is not bounded.
A flight computer needs a hard per-timestep compute budget.
So: excellent as ground truth, unusable as flight code.
Luna · Guided Parafoil Recovery
7 / 16

## Slide 8
ESTIMATION
Wind estimation: the bias killer
Active in the system today. The estimate is formed from the difference between GPS ground velocity and predicted air velocity, then low-pass filtered.
GPS ground velocity
Measured inertial velocity of the vehicle.
− predicted air velocity
What the model says the vehicle should be doing.
→ low-pass filter
Reject gust-scale noise, keep the persistent component.
→ wind estimate
Fed back into prediction so the plan stops drifting.
The filter is the design decision. Too fast and the controller chases turbulence it cannot beat; too slow and a real wind shift is absorbed as steady-state error. Wind is the dominant disturbance, so this single estimator removes the largest source of persistent miss distance.
Luna · Guided Parafoil Recovery
8 / 16

## Slide 9
FAILURE ANALYSIS
Three MPC failure modes — and the fix for each
Failure mode | What goes wrong | Mitigation
Persistent bias | Unmodelled steady wind pushes the vehicle off target every step. | Wind estimator feeding the prediction model.
Constraint violation under disturbance | A nominally feasible plan becomes infeasible once disturbed. | Constraint margin, or tube MPC for a guaranteed envelope.
Terminal-phase model reliance | Near the ground, model error matters most and horizon shrinks. | Sensor-triggered flare instead of model-based prediction.
Each mitigation trades optimality for predictability — and each one is cheap compared with the failure it prevents.
Luna · Guided Parafoil Recovery
9 / 16

## Slide 10
CORE TRADEOFF
SQP versus LTV-QP for flight
 | SQP (`fmincon`) | LTV-QP + OSQP
Method | Iterate linearise → solve → step until convergence. | Linearise once per timestep along a reference, solve one QP.
Accuracy | Higher — handles the nonlinearity directly. | Lower, but sufficient with a good reference trajectory.
Compute | Data-dependent iteration count; no hard bound. | One bounded QP solve per timestep.
Verdict | Development and ground-truth reference. | Preferred embedded formulation for flight hardware.
The migration is driven by compute and reliability constraints, not by control performance. Bounded worst-case runtime is itself a safety property.
Luna · Guided Parafoil Recovery
10 / 16

## Slide 11
TRACK B
Phased waypoint guidance: the option that flies
No optimiser in the flight loop
Behaviour is a direct function of state — inspectable line by line.
Phased structure
Distinct approach phases replace a single global optimisation.
Developed in parallel, on purpose
It is the intended flight-hardware path, not a contingency bolted on late.
Shares the same estimator and actuator stack
Wind estimate and brake-line control are common to both tracks.
What we give up — and get
Give up: constraint handling, optimality, elegant terminal behaviour.
Get: bounded compute, predictable failure, and a control law a reviewer can reason about without running a solver.
For a recovery system, the second column wins.
Luna · Guided Parafoil Recovery
11 / 16

## Slide 12
MECHANICAL
Safety lives in the load path
Core principle
The servo lives only on the brake/control-line branch — never in the primary riser load path.
Flight loads cannot reach the actuator.
Open work
Servo shock-load protection for the control-line actuator.
Locking spool mechanism for the brake/control-line system.
Hard-won lesson: locking geometry
Self-energising pawl geometry is easy to get wrong — the seating moment direction is subtle and an incorrect one locks the wrong way.
Of the locking variants, only the friction brake fails gracefully under shock: it slips rather than transmitting load into the servo.
Graceful failure was chosen over higher holding force.
Luna · Guided Parafoil Recovery
12 / 16

## Slide 13
ROADMAP
What comes next, in priority order
1 · Solver migration
Move MPC from `fmincon`/SQP to an LTV-QP formulation solved with OSQP.
2 · Flare manoeuvre
Rangefinder or barometric trigger, chosen over model-based terminal prediction.
3 · Successive convexification
Possible middle ground between SQP accuracy and LTV-QP compute cost.
4 · Model upgrades
Shear-aware wind prediction; 6-DOF dynamics with apparent-mass terms.
5 · Case study
MIT Underactuated Ch. 10 perching glider — closest analogue to parafoil landing.
Luna · Guided Parafoil Recovery
13 / 16

## Slide 14
TOOLING
Tools and code map
Tool | Role
MATLAB | Primary development environment: `fmincon`, Optimization Toolbox, custom RK4 integrator.
OSQP | Target QP solver for flight-hardware deployment.
Python 6-DOF sim | High-fidelity simulator with LTV-QP MPC, no MATLAB dependency.
MIT Underactuated Robotics | Selective theoretical reference, mined rather than followed.
Key MATLAB files
run_parafoil_mpc.m
top-level MPC run script
simulate_flight.m
closed-loop flight simulation
mpc_parafoil.m
MPC formulation and solver call
parafoil_dynamics.m
vehicle dynamics model
wind_model.m
wind disturbance model
rk4.m
fixed-step RK4 integrator
Luna · Guided Parafoil Recovery
14 / 16

## Slide 15
TAKEAWAYS
Principles worth carrying forward
Feedback beats fidelity
Re-solving on measured state is the robustness mechanism; model polish is secondary.
Bound the worst case
A solver without a runtime bound is not a flight solver, however accurate it is.
Name the failure modes first
Bias, constraint violation, and terminal model reliance each got an explicit mitigation.
Keep actuators out of the load path
Mechanical safety is architectural, not a matter of stronger parts.
Fail gracefully by design
The friction brake and the fallback guidance law exist for the same reason.
Luna · Guided Parafoil Recovery
15 / 16

## Slide 16
Next milestone
LTV-QP MPC on OSQP, validated in the 6-DOF simulator, with a sensor-triggered flare and the waypoint fallback ready to fly.
Questions, and where you think the risk actually is.
Luna · Guided Parafoil Recovery
16 / 16